## Slide 1: Tennessee department of transportation utilization of accelerated bridge construction techniques
Aaron Crowley, Ph.D. KSWA
Travis Smith, P.E. TDOT
Biloxi, Mississippi
November 8, 2016

## Slide 2: Accelerated bridge construction
What is ABC?
Accelerated Bridge Construction (ABC)
  ABC improves/reduces
Why use ABC Technologies?
  Impediments to ABC
  Bridge Farm Concepts
Time Metrics for ABC
TDOT Fast Fix 8 Project
Future TDOT ABC Projects
Fun Fact about the Biloxi Bridge

## Slide 3: What is ABC?
  ABC is a paradigm shift
  Intrinsic Benefits:
    Safety
    Quality
    Durability
    Social Costs
    Environmental Impacts
    From the Owner Agency, perspective may require a change in how a project is approached and how it is justified

## Slide 4: ABC innovation – every day counts
ABC is bridge construction that uses innovative planning, design, materials, and construction methods.
ABC improves:
  Site Constructability
  Total Project Delivery Time
  Work-Zone safety for the traveling public
ABC reduces:
  Traffic Impacts
  Onsite Construction Time
  Weather-Related Time Delays

## Slide 5: Why use abc technologies?
“ABC costs more than conventional”
Owner can’t capture user cost savings
Contractors have a “CIP culture”
Limited early involvement by contractors (legislative limitations)
Durable details are critical

## Slide 6: Why use abc technologies?
Approximately one-fourth of the Nation’s 600,000 bridges require rehabilitation, repair, or total replacement.

## Slide 7: Why use abc technologies?
Bridge Farm Concept Implementation for Fast Fix 8 in Nashville, TN

## Slide 8: Why use abc technologies?
Deck Forming – Continuous Placement

## Slide 9: Why use abc technologies?
Precast Abutments, Piers, and Superstructure Modules

## Slide 10: Why use abc technologies?
Foundation Layout Prior to Demolition

## Slide 11: Why use abc technologies?
Superstructure Module Assembly

## Slide 12: Time metrics for abc
  To gauge the effectiveness of ABC, two time metrics are used:
  Onsite Construction Time:
    The period of time from when a contractor alters the project site location until all construction-related activity is removed.
  Mobility Impact Time:
    Any period of time the traffic flow of the transportation network is reduced due to onsite construction activities.
          Tier 1: Traffic Impacts (Weekend)
          Tier 2: Traffic Impacts (Few Weeks)
          Tier 3: Traffic Impacts (Months)

## Slide 13: Tdot incorporates abc techniques

## Slide 14: Tdot incorporates abc techniques
First CMGC project for TDOT in which the contractor was involved early in the design process
  Completed in four months and 10 weekends
Fast Fix 8 Project is up for AASHTO’s 2016 America’s Transportation Award (Top 12 out of 84 projects last spring)

## Slide 15: Why use abc technologies?

## Slide 16: Future Tdot abc projects
  Two I-24 Bridges in the downtown Nashville, TN loop
    I-24 at Spring Street
    I-24 at Oldham Street and CSX Railroad

## Slide 17: Future Tdot abc projects
  I-24 at Spring Street
  I-24 at Oldham Street & CSX Railroad

## Slide 18: Future Tdot abc projects
  I-24 at Spring Street
  Accelerated Schedule
    TDOT WO: 2-18-16
    Coordination (2-18-16 to 2-24-16)
    Field activities (2-25-16 to 3-3-16)
      8 a.m. to 3p.m.
  9 borings
  120 feet rock coring
  Low headroom under bridge
  Concrete coring

## Slide 19: Future Tdot abc projects
  I-24 at Spring Street

## Slide 20: Future Tdot abc projects
  I-24 at Oldham Street & CSX
  Accelerated Schedule
    Coordination (2-18-16 to 2-24-16)
    Field activities (2-26-16 to 6-8-16)*CSX delays
      Day/night drilling
      Only 14 days of actual drilling
  16 borings
  200 feet rock coring
  Drilling under bridge
  Asphalt coring

## Slide 21: Future Tdot abc projects
  I-24 at Oldham Street & CSX

## Slide 22: Future Tdot abc projects
  I-24 at Oldham Street & CSX

## Slide 23: Thanks
Aaron Crowley, Ph.D. KSWA
Travis Smith, P.E. TDOT
Biloxi, Mississippi
November 8, 2016

## Slide 24: Fun fact: Biloxi bridge