## Slide 1
History & Practical Applications of GRS/GCS Structures
Nate Beard, P.E.
Matt Reihl, P.E.

## Slide 2
HISTORY

## Slide 3
What is GRS or GCS?
Geosynthetically Reinforced Soil (GRS)
Geosynthetically Confined Soil (GCS)
An engineered fill of closely spaced alternating layers of compacted granular fill.

## Slide 4
HISTORICAL USE OF REINFORCED SOIL (200 BC)
Section of the Great Wall of China constructed using layers of grass and Tamarisk (willow) twigs to reinforce granular soils

## Slide 5: ziggurats 1440 BC
Soil Reinforcement is a Very Old and Proven Technology

## Slide 6
U.S. FOREST SERVICE
First use of geosynthetics to stabilize logging roads

## Slide 7
U.S. FOREST SERVICE – FIRST USA FABRIC WALL

## Slide 8: TESTING
Cheesecloth reinforced soil (CRS) structure supporting 10 tons.
Test without cloth failed when second block was placed.
“Bedsheet” Reinforced Soil (BRS)

## Slide 9: RESEARCH
Largest GCS Research Wall, 1982

## Slide 10: RESEARCH
Calculated Factor of Safety of 0.1
AASHTO applies to MSE not GRS

## Slide 11: FHWA Research center
GCS Bridge Pier exceeded 10 tons per square foot bearing capacity.

## Slide 12: Composite failure
FHWA Mini-Pier Experiment
Photo courtesy of M. Adams

## Slide 13
GCS™
Composite Structure
Internally stable
Friction Connections
Lightweight Inclusions
Close spacing
High Safety Factor
MSE
Reinforced Soil Structure
Quasi-tieback
Pin Connections
Strong reinforcement
Wide Spacing
2-10% Failure Rate
Comparison between GRS/GCS and MSE

## Slide 14
H
B
B
B/H ≥ 0.7
B/H ≥ 0.3
4” 8” 12” 16” 20” 24” 28” 32”
Sv =
MSE
GRS
Composite
Tie-back
Reinforcement spacing
Notes: Zone of influence
The “grey” area has not been fully defined yet; it is a function of soil properties, reinforcement type, and degree of compaction

## Slide 15
0.5 ksf
(25 kPa)

## Slide 16
4.1 ksf
(196 kPa)

## Slide 17
5.9 ksf
(282 kPa)

## Slide 18
8.5 ksf
(407 kPa)

## Slide 19
11.3 ksf
(541 kPa)

## Slide 20
15.3 ksf
(733 kPa)

## Slide 21
18.1 ksf
(867 kPa)

## Slide 22: 2400 lb/ft @ 8” Spacing, No CMU Facing, <0.5% strain 18,000 lb/ft shown in Post-Picture
Pre-
Post-
Performance test

## Slide 24
Reference materials
The Science
(Research)
Application
(Engineering)
Sample Guide

## Slide 25
APPLICATION

## Slide 26
Bridge abutments

## Slide 27
GRS Benefits
Reduced Construction Cost (25-60%)
Reduced Construction Time
Less Weather Dependent
Field Modified Design – Flexible
QA/QC Advantages
Bridge Abutment Construction

## Slide 32
Interrupt Sediment Transport
Washout
Constricted channels
Inlet Ponding
Hydraulic Uplift
High Velocity Flows
Scour
Waterfalls
Barriers to Fish Passage

## Slide 33: Box culverts
Higher flows while addressing many environmental concerns

## Slide 34
GRS ARCH

## Slide 35
Stream Realignment

## Slide 36
Shoulder Failure

## Slide 37: Complete Roadway reconstruction

## Slide 38: Remote access

## Slide 39: Guardrail & guiderail

## Slide 40: NEGATIVE BATTER

## Slide 41: SETTLEMENT

## Slide 42: GREEN AESTHETICS

## Slide 43: Where is it?

## Slide 44: Vegetation Faced

## Slide 45: Natural stone

## Slide 46
NATURAL STONE

## Slide 47
NATURAL STONE

## Slide 48
COMBINATION OF BLOCK AND NATURAL STONE

## Slide 49
BARRIERS

## Slide 51: Impacted by 2700 cubic metre rockslide

## Slide 57
CASE STUDY – Laurens County, GA

## Slide 58
The Site Had a number of unique challenges
Bearing Capacity
  2,500 psf
  Clayey Sands & Silty Sands
Fine Sands/Silts = Scour Concern
Budget
Contract Delivery
  GSI Design Abutments
  Contech – Superstructure
  County Forces Build.

## Slide 59
Georgia is ranked average in its bridge inventory

## Slide 60
The existing bridges were in a state of disrepair

## Slide 61
The existing bridges were in a state of disrepair

## Slide 62
Scour

## Slide 63
Scour micropiles ® prevent scour

## Slide 64
Scour micropiles ® prevent scour
1 Day of Drilling Per Abutment

## Slide 65: Drilled Soil Nails w/ hollow bars

## Slide 66: GRS-IBS Bridges have survived floods
Mount Pleasant Rd. Huston Township, Clearfield County, Pa.

## Slide 67: GRS-IBS Bridges have survived floods

## Slide 68
Upstream Left
6/6/14
7/8/13
Rip-rap position comparison study

## Slide 69
Scour micropiles ® & Rip-Rap

## Slide 70
Bearing pressure – increase bridge footprint

## Slide 71
FHWA’s publications - valuable insight
FHWA – No less than 8 Specific Tools for Engineers are available on the Every Day Counts website.

## Slide 72
FHWA – Instrumented Bridges – settlement?
Majority of settlement occurs during dead loads & before open to traffic.

## Slide 73
FHWA – Instrumented Bridges – settlement?
Many more bridges have been instrumented and results are consistent

## Slide 74
Pumping??? No Problem!
GRS Construction inherently uses the benefits of geotextiles and granular fills to:
  Drain Saturated Soils
  Relieve Pore Pressures
  Re-establish Particle-Particle interaction

## Slide 75
Sunshine Hill Bridge – Foundation Excavation

## Slide 76
Sunshine Hill Bridge – Foundation Excavation

## Slide 77
Remain calm, use the tools in your toolbox.
The combination of well drained, fractured-faced granular materials and geotextiles is highly effective.

## Slide 78
Before and after – sunshine hill bridge

## Slide 79
Back to laurens county, ga

## Slide 80
Teaching The County Forces to Build
So Easy Detainees can do it!

## Slide 81
Invest in the first course…Everything bears on it!

## Slide 82
Production Rates Improve after 1st course

## Slide 83
Smooth and compact by hand

## Slide 84
Next compact w/ vibration

## Slide 85
Production Rates Improve after 1st course

## Slide 86
Concrete beam seats for steel superstructureS

## Slide 87
PlanNED For Deflection of Superstructure

## Slide 88
Almost open

## Slide 89
Budget & Contract Delivery
Budget:
  Early Projections 40-50% savings.
Contract Delivery Methods:
  Empower the county to construct as much as possible
    Buy Materials
    Use County Forces
    Use County Labor Resources (Detainees)
Communicate!
  Simple Design & Construction doesn’t mean less communication
  Coordination between design and construction groups is essential.
Every Day Counts…. Remember this during design and specification
  Replace more bridges with less funds for safer roads for our families.

## Slide 90
Thank you!! Questions??