## Slide 1: Foothills Parkway Micropiles Support Closing the Missing Link
by
Anthony Sak, P.E.
STGEC 2016
Biloxi, Mississippi
November 9, 2016

## Slide 2: Presentation Outline
Introduction
Parkway History
Project Overview
Site and Subsurface Conditions
Micropiles
Project Foundation Construction

## Slide 3: But first, just a little about us…
Hayward Baker Inc. (HBI) is North America’s leading specialty geotechnical contractor, offering the full range of pre and post-construction services.
  Foundation rehabilitation, settlement control, soil stabilization, excavation support, etc.
US headquarters are in Hanover, MD (Baltimore area)
  Annually ranked #1 in our field by Engineering News Record
Keller Group plc is Hayward Baker’s parent company headquartered in London.
  Publically owned and traded on the UK stock market
  Offices in over 40 countries on 6 continents

## Slide 4: Hayward Baker’s National Presence

## Slide 5
THINK SAFE
WORK SAFE
GO HOME SAFE
Goal: Zero Injuries

## Slide 6: Geotechnical Problem… Hayward Baker Solution

## Slide 7: Parkways in the Southeast
Smoky Mountain National Park (NC side) to Shenandoah National Park (Virginia) – 469 miles
Construction from 1935 to 1987

## Slide 8: Parkways in the Southeast
Natchez, MS to Nashville, TN – 444 miles
Construction from 1938 to 2005

## Slide 9: Parkways in the Southeast
North side of Smoky Mountain National Park (TN side) – 72 miles
Construction from 1960 to ?

## Slide 10: Foothills Parkway History
Congress authorized – February 22, 1944
  Provide beautiful vistas of Smoky Mountain NP
  Disperse visitor traffic
Two lane, 72 miles in 8 segments (A-H)
Initial construction began in 1960’s; sections A and G to H open
Construction of Segments E and F (16.1 miles) begin in 1984 and 1985
Segment E contract terminated in 1989
  MSE retaining wall failures
  E&S problems leading to acid runoff from pyritic rock
The 1.65 mile “Missing Link” is born

## Slide 11: Foothills Parkway History
1990’s Missing Link redesigned by FHWA:
  Minimize surface disturbance and environmental impacts
  Mitigate previous erosion and wall problems
  Series of 10 bridges (1 through 10)
Bridges 1, 2, 8 – 10 completed 2001 through 2012
Bridges 3 to 7 under construction
  Design-build delivery - $46.2 million contract
  Contractor - Lane Construction
  Designer - HDR
Future final paving, safety, and signage of Segments E and F (est. $30M)
Sometime in the future… the final 30 miles

## Slide 12: Where is the Missing Link?
Missing Link
16.9 miles
5.6 miles
16.1 miles
Notes: Insert your content/slides.

## Slide 17: Missing Link Bridges
Notes: Insert your content/slides.

## Slide 18: Bridge Design
Bridge 3 - Single span, 158.5 feet
  Both abutments founded on micropiles (MPs)
Bridge 4 - Two span, 290 feet
  Abutment 1 and Pier 1 founded on MPs
  Abutment 2 founded on spread footings
  Pier 1 – permanent rock dowel SOE
Bridge 5 – Two span, 336.5 feet
  Founded on spread footings
Bridge 6 – Single span, 215 feet
  Both abutments founded on spread footings
Bridge 7 – Single span, 215 feet
  Both abutments founded on MPs

## Slide 19: Pre-Construction Site Conditions

## Slide 21: Subsurface Conditions
Meta-sandstone, meta-conglomerate, and occasional phyllite
Residual soil – 0 to 15 ft thick
Highly weathered rock (50 blows < 6 in) – 0 to 10 ft thick
Fractured rock
Competent rock – depth varies 20 to 45 feet
  REC > 85%
  RQD > 50%

## Slide 22: Micropiles: Overview
Micropiles
Structural Load Bearing Elements
Usually drilled-in
Installed vertical or battered
Capacities as little as 3 tons to more than 500 tons
Depths of 200+ feet
Also known as minipiles, root piles, pipe piles, etc.

## Slide 23: Micropiles are routinely used for:
New Construction
Underpinning existing Foundations
Limited access or low headroom
Foundations where obstructed drilling is required
Deep foundations in Karst Geology
Replacements for failed existing deep foundations
Seismic Retrofit
Slope Stabilization

## Slide 24: Micropile Materials
Permanent Steel Pipe
  API N80 & ASTM A252
  80 ksi yield
  Flush joint threads
Steel Reinforcement
  ASTM A615, Gr. 60 & 75 80, 95 & 100
  ASTM A722, Gr. 150
  Mechanical coupling
Cement Grout
  Neat cement – ASTM C150
  W/C ratio of 0.45
  4,000 psi (min)

## Slide 25: MP Installation

## Slide 26: Micropile As-Designed

## Slide 27: As-Designed
vs.
Value- Engineered

## Slide 35: MP Testing
Verification compression load test
  Sacrificial MPs
  2 x the design (unfactored) load ~ 430 kips
Tension proof load test
  Production MPs
  1.6 x design (unfactored) load ~ 344 kips

## Slide 38: How were the Bridges Constructed?
Cast-in-place, post-tensioned box girders

## Slide 40: How were the Bridges Constructed?
Cast-in-place, post-tensioned box girders
Since CIP, need temporary falsework
Falsework needs foundations

## Slide 43: How were the Bridges Constructed?
Cast-in-place, post-tensioned box girders
Since CIP, need temporary falsework
Falsework needs foundations

## Slide 44: Falsework Foundations
GC set work platforms at each location

## Slide 45: Set Small Drill Rig on Platform

## Slide 53: Falsework MP Cap with Columns

## Slide 56
Questions?
Tony Sak, PE
asak@haywardbaker.com