## Slide 1: A Hybrid Retaining Wall to Conquer a Massive Slope
Birmingham northern beltline
SR-959

## Slide 4: PROJECT OVERVIEW
Portion of the future northern beltline between Highways 75 & 79
Overall project estimate is $5 billion
Estimated completion date is 2054 +/- a few months
This Phase of work was $46 million
Rolling terrain with several cuts into mountainous terrain
Most difficult wall was 150’ tall with a cost of $6 million
ALDOT performed extensive geotechnical investigation work
Final wall design was up to the contractor
Wright Brothers Construction was the successful prime contractor
  Russo Corporation was the successful wall contractor
  Schnabel Engineering hired by Russo to assist with wall design

## Slide 6
ALDOT PLAN
Notes: Plan view of the walls. Roadway. 4 tiers with 3 benches. There is also a drainage ditch that runs along the top of wall

## Slide 7
Rock included:
Limestone
Shale
Sandstone
Iron ore
Chert
Soils included:
Transition zones (weathered soils)
Silty sands
Clayey sands
Silts
Sands
Lean clays
Cherty clays
Notes: Extensive geotechnical exploration and geologic mapping was performed by ALDOT. This is an elevation view of the wall. Since this is a mountain, there is a well defined rock core. As defined in the geological group, the rocks included in the mountain rock core were limestone, shale, sandstone and chert. This rock mass was as if you took a stratigraphy with horizontal bedding and turned it 90 degress.
Soils also varied from Silty and clayey sands, Lean clay and cherty clay.
This picture shows the variability of the residual soils in a very small portion of the wall.

## Slide 8
REQUIRED SOIL NAIL WALL
~150 ft
40 ft
20 ft
Bid documents
EXISTING GRADE
Notes: Original project intent from ALDOT was to make this wall a traditional soil nail wall. Again, the maximum height of the wall was approximately 150 ft. Russo approached Schnabel to request potential design assistance and VE alternatives. The basic soil nail design approach was producing soil nails that were too long.

## Slide 9
150’
20’
WALL LENGTH ~1000’
Hybrid
approach
TIE BEAM
SHOTCRETE FACE
STRAND ANCHOR
SOIL NAIL

## Slide 10
Notes: Ran slope stability analyses and confirmed that there was deep global stability failure surface that was 30-40 ft deep without any support. When you model your nails, we found out that very long nails were required to accomplish a FS of 1.5 for the long term condition. That's when we decided to combine two technologies and design a hybrid wall.

## Slide 11
Notes: we took care of the deep global stability issue with long tiebacks and handle the shallow global stability of each wall with soil nails.
Global stability target FS was accomplished with 3 levels 245 kip tieback at 6 ft o-c.

## Slide 12
Notes: shallow global stability target FS of the walls was accomplished with short soil nails. This was cheaper and more effective solution than the initially proposed.

## Slide 13
Soil Nails
  6V:6H Spacing
  #11 Bars
  20 ft, 25ft and 35 ft long
Tiebacks
  6 ft o-c Spacing
  7 Strands (245 kip)
  80 ft long
Temporary Facing
  Shotcrete
  5 inch thick
  W5 x W5 WWM
Permanent Facing
  Shotcrete
  5 inches thick
  W5 x W5 WWM
  No Shear Studs!!
Notes: All the wall components are Soil nails, Tiebacks, Permanent facing (due to project requirements and schedule we designed the permanent facing as two layers of shotcrete 5" thick each. First layer was considered very temporary. The contractor shot the first layer, set the plates an tighter the nuts, then came back when the shotcrete was at least 500 psi and shot the final 5 inches. Then they proceeded to excavate the next lift. Each lift was completed with a final facing before the next one was excavated. we were able to accomplish this without the use of headed studs

## Slide 14
Notes: Other important components were a tie-beack used to support and distribute the load from the tiebacks; eventhough all the borings were being dry, We installed 20' long subhorizontal drains and drainage strips

## Slide 16
Soil Nails
  325 - 20 ft long nails
  552- 25 ft long nails
  676 - 35 ft long nails
  Total Soil Nails = 1552
Tiebacks
  136 - 80 ft long tiebacks
Load Testing
  5 Verification Test Nails in Rock
  3 Verification Test Nails in Soil
  2 Verification Test Tiebacks

## Slide 17
What we tested:
  Tiebacks
  (bonded deep into rock)
  Design LTR = 8.4 kips/ft
  Soil Nails
  (bonded near surface)
  Design LTR = 8.4 kips/ft
Design Assumptions
  Anchors could achieve a design load transfer ratio (LTR) of 8.4 kips/ft
Verification Test Program – Load Test Ratio
Notes: Initially, we developed a load testing program based on a load transfer ratio of 8.4 kip/ft for the residual soils and rock. Which was based in local experience. Since the geology was very variable, several load tests were required.

## Slide 18
Nails instrumented with strain gauges
Unbonded zone by PVC
Nail head deflection measured with 2 dial gauges
Applied load confirmed by load cell
Nail Verification Test
Notes: with the strain gauges we could determine the load distribution through the bond zone and get the allowable LTR

## Slide 19: Soil Nail Verification Load Testing

## Slide 20
Nail | Design Maximum Test Load (kip) | Maximum Load Achieved (kip) | Design LTR (kip/ft) | Achieved Allowable LTR (kip/ft) | Soil in Bond Zone
VT1 | 168 | 168 | 8.4 | 13.7 | Chert
VT2 | 168 | 168 | 8.4 | 13.3 | Weathered Shale
VT3 | 168 | 210 | 8.4 | 12.8 | Weathered Shale
VT4 | 168 | 126 | 8.4 | 6.3 | Cherty Clay/Weathered Chert with Clay
VT5 | 168 | 115 | 8.4 | 5.75 | 
VT6 | 200 | 270 | 13.5 | 13.5 | Weathered Sandstone
VT7 | 270 | 270 | 13.5 | 13.5 | Chert
Nail spacing was changed from 6 ft on center to 4 ft on center; ~35% increase in nails
Nail Verification Test Results
Notes: We started with the load test program and it everything was perfect. The first 3 testes were predominantly in chert and weathered shale. Then the following two tests failed. These testes were in cherty clay and highly weathered chert with clay. Due to the failed tests, the spacing of the nails was reduced in approximately 35% for the nails in residual soils.

## Slide 22
Notes: Nails drilled with a down-the-hole hammer attached to an excavator, air flushed. They also had a casagrande rig with the same 8" DHH. In this picture you can also see the epoxy coated nails every 4 ft and the drainage strips.

## Slide 29
Notes: Days before the picture, there were heavy rains in the area. This amount of water was visible in two relatively small zones of the wall and is evident that the drainage strips and horizontal drains are working.